PART 1 - GENERAL

1.1	RELATED SECTIONS:

Refer to Section 10800 for the requirements relating to toilet accessories.

Refer to Section 15400 for the requirements regarding plumbing systems, including plumbing fixtures.

1.2	SCOPE OF SECTION:

This section contains the requirements for enclosures, dividers, and screens for use in conjunction with toilet compartments and urinal screen walls in toilet rooms.

  - TOILET ROOMS:

- PARTITION MATERIALS:

  - All partition materials shall utilize either 1” thick solid plastic (HDPE) or ¾” thick solid phenolic, sized per the drawings.

  - Solid plastic unit color to be homogenous throughout.  Color to be selected by Designer with consultation with Project Manager.

- MOUNTING TYPE:

  - Toilet compartments shall be floor-mounted, overhead braced.

  - Urinal screen walls shall be wall-mounted, floor braced.

    - All hardware utilized shall be institutional type, heavy duty, corrosion proof and of tamper-proof design.  Installations shall be done to resist daily abuse in a typical university/school environment without damage.  This typically means, aluminum, continuous length, double-eared wall brackets, continuous length, spring-loaded, piano-type hinges, door bumpers and other non-specified accessories.  When dealing with renovation projects or projects where compartment panels or urinal screen walls are attached to building partitions with uneven or tiled surfaces, Contractor shall install with multiple (minimum of three), individual double-eared wall brackets, in lieu of continuous length wall brackets.

- Mechanical fasteners shall be sufficiently sized to rigidly anchor wall/floor brackets to substrate and prevent anchor failure.  The typical manufacturer supplied screw fasteners with nylon anchors are not to be used to support wall/floor brackets as they normally don’t meet this requirement.

- In gypsum or plaster constructed walls with metal/wood framing members, sufficient blocking shall be provided to receive mechanical fasteners mentioned above.

- All exposed hardware shall be of stainless steel or aluminum construction.

- The mounting of panels, doors, etc. to wall brackets, pilasters, head-rail brackets, etc. shall be done by through-bolting with one-way, stainless steel, sex bolts.

- No cadmium plated bolts allowed.

  - At floor mounting points, provide manufacturer’s standard corrosion resistant supports, leveling mechanisms, fasteners, and anchors at pilasters to suit floor conditions.  Provide stainless steel, mechanically fastened, shoes at all pilasters to conceal anchorage.  Where anchorage devices, threaded rods, etc. penetrate floor finishes, provide elastomeric or silicon caulking to seal holes, prior to installing shoes.

  - Installation of all partitions shall be in accordance with the manufacturers standard written instructions making sure of the following:

    - All parts shall be installed in a substantial, rigid manner making sure all edges are straight, level and plumb.

    - Clearances between adjacent vertical edges shall be uniform, top to bottom, and shall not exceed 3/16”.

    - Finished product shall show no evidence of drilling, cutting or patching.

    - Lubricate and adjust swing of doors to match that shown on plans or as directed by Designer.  This typically means the HC stall shall remain in the closed position, when left unlatched, and the other stalls shall remain approx. 30 degrees open when left unlatched.

    - Finished surfaces shall be cleaned after installation and left free of imperfections.

- Contractor is to maintain protection of partition finishes during course of construction or until project is accepted by Owner.  At that time, protective plastic wrapping or other protective devices can be removed.

END OF SECTION