# PART 1 - GENERAL

1.1	RELATED SECTIONS:

Refer to Section 02085 for the requirements on labeling insulation to indicate the presence or absence of asbestos.

Refer to Section 02600 for requirements relating to the identification of underground piping and utilities described in Division 2.

Refer to Section 10440 for interior signs.

Refer to Section 15190 for requirements regarding identification of mechanical items described in Division 15.

Refer to Section 16195 for electrical identification.

Refer to ECU Facilities Services Standard Practice 34-0001 for building names and other sign information.

1.2      GENERAL:

East Carolina University has adopted a standard policy and design for all exterior signs erected on campus; refer to the drawings included in this Section for typical signs.  Permanent signs required by a project but not referenced here shall be submitted to Facilities Services for approval.

Products shall be equal or exceed in quality to the signs existing on campus including the sign installed at the Rivers Building and the directory installed at the Spilman Building on the Main Campus of East Carolina University.  Signs and directories shall be reviewed at the site visit.

  - SCOPE OF SECTION:

The School of Medicine has provided signs on Health Sciences Campus.  However, preliminary design following this Standard shall be submitted for signage on the Health Sciences Campus for review.

This Section contains the requirements for exterior signs used in establishing identity and communication.  Included are exterior signs of the following types:

- Directories (Sign Type A)

- Campus entrance sign/Welcome sign (Sign Type B)

- Building sign/Major Zone signs (Sign Type C)

- Small Building/Historic District signs (Sign Type D)

- exterior ada Directional signs (Entrance Sign).

1.4	SIGN DESCRIPTION:

- Directories (Sign Type A):

This type of sign is used to provide a campus map and show locations and names of all buildings on campus and referenced map location.

- Campus entrance sign/Welcome sign (Sign Type B):

This type of sign is used to welcome visitors upon arrival at the campus and to delineate boundaries.  The sign can be externally lighted.

- Building sign/Major Zone signs (Sign Type C):

Building signs identify campus buildings by official name.  See ECU Facilities Services Standard Practice 34-0001 regarding the naming of buildings.  Major zone signs define areas and sites for student activity on campus property.

- Small Building/Historic District signs (Sign Type D):

This type of sign is a smaller version of the welcome and building identification signs.  This type of sign is used on small campus buildings as determined by Facilities Engineering and Architectural Services.  Signs within the Historic District are installed after obtaining a Certificate of Appropriateness from the Historic Preservation Committee, City of Greenville Planning and Community Development Office, and the Division of Archives and History, State Historic Preservation Office in Raleigh.

- exterior ada Directional signs:

Directional signs indicate ADA accessible entrances, non-accessible entrances, and/or directions to an accessible entrance.  These signs shall conform with ADA Guidelines, ECU Facilities Services Standard Practice 34-0001, and Facilities Services.  Facilities Services, in consultation with appropriate parties, shall determine location of these signs.  The Project Architect/Design Consultant for new buildings shall be responsible for identifying accessible entrances and routes to the entrances.  Contractor shall provide and install appropriate signs.

The Attachments provide a general description, specifications, and pictorial view of each of the Sign Types A, B, C, and D.  Detailed specifications are available from Facilities Services.

1.5	GRAPHIC STANDARDS:

This section provides graphic standards for Sign Types A, B, C, and D.  Standards for exterior ADA directional signs (entrance signs) shall be approved by Facilities Services with regard to the specific building.

- Color:

- The color of the logo, lettering, and graphics shall be black, equal to standard 3M vinyl #220-12, black.

- The color of the posts shall be PMS 433C dark gray with acrylic polyurethane satin gloss finish.

- The color of the sign face is to match PMS 428C light gray.

- Lettering:

- The East Carolina University logo on the sign is registered as a legally protected trademark of the University and shall be produced from authorized originals without being modified.

- All copy shall be ITC Garamond (True Type Version).  A number of standard letter sizes have been established which should be appropriate for most signage needs.  The letter size depends on the reading distance and the surrounding environment; vehicular or pedestrian traffic also have a bearing on letter size.  The letter height selected shall be based on field testing, since environmental considerations, placement, viewing distance and angle can vary between locations.  The following sizes, however, shall generally be used.

- Lettering heights on directories shall match that as on existing directories.  Contact Facilities Engineering and Architectural Services for location of these directories on campus.  East Carolina University lettering shall be one and one-half inches (1 ½”).

- Campus entrance signs shall generally be viewed by vehicular traffic at speeds of 30-35 mph and should have lettering sized a minimum of two and one-half inches (2 ½”) and three and one-half inches (3 ½”) for lettering as shown on attachment.

- The minimum cap height for building/site names shall be three and one-half inches (3 ½”).  Sub-titles shall have two-inch (2”) letters.

- Small identification signs shall have two and one-half inches (2 ½”) lettering.  Small scale buildings and buildings in the historic district shall have small identification signs.

- Height:

The height of the top of signs shall be as follows:

- Sign Type A:  The top of a directory sign shall be 9’-0” above grade.

- Sign Type B: 4’-1” for Welcome signs in softscape (shrubs).

- Sign Type B: 3’-1” for Welcome signs in hardscape (grass and hard surfaces.

- Sign Type C: 4’-1” for Building signs in softscape (shrubs).

- Sign Type C: 3’-1” for Building signs in hardscape (grass and hard surfaces.

- Sign Type D: Small signs (5’-2 1/2” wide) shall be 2’ – 31/2’ to top of sign.

1.6	FABRICATION:

## SIGN TYPE A (SINGLE FACED) DIRECTORIES:

Fabricate back panel from .08 aluminum with no seams or defects.  Front panel ¼” thick white acrylic panels with vinyl lettering except For EAST CAROLINA UNIVERSITY at the top. Provide vinyl decal on ¼” thick white acrylic panel (match existing directory).  Fabricate posts from extruded aluminum (1/8” wall) with no seams or defects.  Protective cover is to be fabricated from 1/8” thick lexan.  Sign Type A only is to be illuminated with five-tube fluorescent lighting with electronic ballasts and T-8 bulbs.  Match existing ventilation.  Provide waterproof junction box below grade.  Provide ground wire and wiring according to the National Electrical Code.  Sign shall be UL listed and show UL label on the directory.

## SIGN TYPES B, C, AND D:

Signs are to be double faced and fabricated from .08 aluminum reinforced with .125 aluminum frame.  Post attaches to frame with interlocking track.  Faces shall be free from fasteners or seams.  Countersink vandal resistant fasteners where fasteners are required.  Posts shall be .125 extruded aluminum with no seams or defects.

- Exterior finish and graphics shall be acrylic polyurethane.  All finishes shall be even and smooth.

- All metal-to-metal connections shall be tight.  Provide detailed shop drawings, sample materials for review by Facilities Engineering & Architectural Services prior to fabrication.

1.7	PLACEMENT:

Placement and location of all signs shall be approved by Associate Vice Chancellor for Administration and Finance – Facilities via Project Manager.

- BUILDING NAMES:

Refer to ECU Facilities Services Standard Practice 34-0001 regarding building names.

- RESPONSIBILITIES:

- Capital construction projects shall provide funding to pay for the signs associated with each project.

- In capital construction projects, the General Contractor shall be responsible for contracting manufacture of and for placement of the signs on campus in compliance with the policies and specifications outlined in this document and ECU Facilities Services Standard Practice 34-0001.

- The Contractor shall be responsible for full replacement for defects in materials or workmanship for five years.

- Budget entities and auxiliaries shall be responsible for paying for the costs of requested signs for existing buildings.

  - UPDATES:

### SIGN TYPE A UPDATE:

Remove and replace the campus map, plastic back, and " EAST CAROLINA UNIVERSITY" letters at the top.  Computer Graphics for the map shall be provided by East Carolina University in Adobe illustrator (Macintosh).  It shall be the responsibility of the sign contractor to plot the map graphics.  Match existing directory graphics.