# PART 1 - GENERAL

1.1	RELATED SECTIONS:

Refer to Section 02085 for the requirements on labeling insulation to indicate the presence or absence of asbestos.

Refer to Section 10430 for requirements on exterior signage.

Refer to Section 15190 for requirements regarding identification of mechanical items.

Refer to Section 16195 for electrical identification.

Refer to Appendix E for the current interior signage specification titled Interior ADA Compliant Signage Program.

1.2	SCOPE OF SECTION:

This section applies to Main Campus and West Research Campus.  This section contains the requirements for signage identifying the name, number, occupant, and/or function of interior rooms, spaces, and furnishings. Wayfinding signage and graphics shall be incorporated into the design for room identification, directories and directional signage including those addressing emergency egress routes.  It also contains the procedures and conventions used in assigning room numbers.

The School of Medicine has provided signs on Health Sciences Campus.  However, preliminary design following this Standard shall be submitted for signage on the Health Sciences Campus for review.

1.3	SYSTEM DESCRIPTION:

- All signs shall be in conformance with ADA Guidelines.

- All rooms and spaces on the campuses shall be identified by numbers, which are considered the permanent title of that room or space.

- Provide sign with legend "NO EATING OR DRINKING" in each classroom.

- Special function rooms or spaces, e.g. toilets, elevators, housekeeping closets, and mechanical and electrical rooms, shall have identifying signs.  Data and telecommunication closets shall be labeled with a room number.

- Public area bulletin boards shall be in enclosed lockable cabinets matching existing as appropriate.  Any additional bulletin boards or signs identifying occupants shall be provided only when directed by Project Managers.

- Pictograms shall be included on signs for toilets, elevators, accessible phones and elsewhere where required by ADA or as deemed appropriate or desirable.

- All fixed seating shall be numbered and have identifying signage on each seat.  Each row of seats shall be numbered and have identifying signage at each entrance to the row.

1.4	ROOM NUMBERING:

- Main Campus and West Research Campus:

Room numbering conventions have been developed and are generally followed throughout the University for the purpose of standardizing University room numbering.  It is intended that these conventions be both specific enough to accomplish standardization and general enough to apply to a wide variety of situations with the flexibility necessary to create logical "user-friendly" room numbering schemes.  Room numbers and space numbers are to follow a simple logical sequence.

Room numbering for new and renovated facilities shall occur during the design process to ensure that bid and as-built drawings display room numbering established according to University conventions.  The Designer shall be responsible for assigning room numbers on design drawings according to conventions given below for review and approval by the University.

- Generally a 3-digit number is used, with the first digit signifying the floor number. For large buildings a 4-digit number may be used, if necessary.  For smaller buildings, where expansion of the building or subdividing the rooms is unlikely, 2-digit or 1-digit numbers may be used.  A letter prefix may be added to the room numbers to designate an area, floor, or wing of the building.  Floors located predominantly below grade and below the floor where the main entrance is located shall be designated with the prefix "G".  Do not use decimals or fractions to designate intermediate levels.  All accessible spaces including housekeeping, mechanical, electrical, bathrooms, chases, data & telecommunication closets, and other closet spaces shall have assigned room numbers.

- Generally, on buildings designed with a central corridor layout, even numbers are used on one side of the corridor, odd numbers on the other.  On more complex designs, the "odd-even" format shall be abandoned if consecutive numbering shall result in a more logical "user-friendly" scheme.

- Skip a number for every 10 feet of corridor, to accommodate future partitioning of rooms.  Also, skip numbers as necessary to keep rooms on opposite sides of a corridor in approximate sequence.

- Generally, rooms that are accessed only through another room (not through circulation space) are given the same room number as the room they are accessed through, plus a letter suffix.  The first such room (reading from left to right from within the primary room) is assigned the suffix "A", with subsequent rooms being assigned the suffixes "B", "C", and so on.  (i.e. A room that is accessed only through Room 250 is designated as Room 250A.)

- Avoid “I,” “O,” and “Q” which may be interpreted as numbers.

- Staircases are not given floor or room numbers and shall be identified “Stair 1,” “Stair 2,” “Stair 3,” etc.  Elevators are not given floor or room numbers and shall be identified “Elevator A,”  “Elevator B,”  “Elevator C,” etc.

- The Designer shall identify corridor numbers for construction, maintenance, and reporting purposes only; corridor numbers shall not be posted.  The sequence used for corridors shall not affect the sequence for rooms.

- Make the room numbering system as consistent as possible from floor to floor.

  - Health Sciences Campus:

    - The room numbering system for the Brody Medical Sciences building is as follows:

- The first character is the floor, and is the letter G or numbers 1 through 8.

- The second character is a letter, A through H, J through L, N, S or W.

- A through D, F through H, J and K designate modules in the Brody Outpatient Center.

- E, N, S and W designate to the east, north, south and west halls on each floor.

- L designates the Laupus Health Sciences Library.

- The remaining characters designate the room number, with a suffix letter designating subdivisions of a room or suite.

- There is one exception to this system.  In the administrative suite on the first floor of the library building, the rooms are designated AD-##.

  - Other buildings on the Health Sciences campus follow the same room numbering scheme as on Main campus.

1.5	PROJECT CONDITIONS:

- Match existing signs in renovations and adhere to ADA requirements.

- Tactile (raised text) signs and directories are preferred if located within reach of pedestrians.  Signs not required to meet ADA requirements as to raised text are still preferred to have raised text.

PART 2 - PRODUCTS

Refer to Appendix E for the current interior signage specification titled Interior ADA Compliant Signage Program.

PART 3 - EXECUTION

  - GENERAL:

- Refer to Appendix E for the current interior signage specification titled Interior ADA Compliant Signage Program.

- All signs shall be mounted in accordance with ADA compliance.  Any deviations shall be approved by Project Manager.

- Locate signs on the wall adjacent to the latch side of the door.  Do not put signs on doors.

- If sign must be affixed to glass, provide a back-up panel the same size as the sign and holder on the other side to hide adhesive.

- Signs and sign text denoting room numbers, toilets and mechanical rooms are considered permanent, all other information on signs is subject to change.

- Remove existing signs if new signs are being installed at that location or area; repair substrate to match surrounding area.

  - INSTALLATION:

Refer to Appendix E for the current interior signage specification titled Interior ADA Compliant Signage Program.

END OF SECTION