- PURPOSE

The purpose of this plan is to optimize energy conservation while maintaining adequately conditioned space.

- SYSTEM DESCRIPTION

- AIR HANDLING UNITS

AHU#	RM#	Area Supplied	Area Description

- HVAC CONTROLS

  - SEQUENCE OF OPERATION

The HVAC system is controlled by an Invensys DMS-3500 system, connected to the Ethernet and an Ultivist operator workstation at the Steam Plant for control and alarm monitoring.

    - There is a main steam valve, which is opened with temperature decrease that allows the three wings to be heated.  This controlled by the BAS.

    - The three zones are enabled on load demand and controlled by a sensor in each zone.  Each of these three zones is controlled by the BAS’

    - The domestic hot water system is monitored only by the BAS system.

  - LOAD MANAGEMENT

There is no load management in this building.

- COOLING SYSTEM

Window units in offices and resident advisors rooms to provide cooling.

- HEATING SYSTEM

The heating in this building is steam radiators in each room controlled by a manual valve.  The BAS controls the zone steam valves based on outdoor air and zone load.

- SPECIAL OPERATING INSTRUCTIONS

The domestic hot water system is a stand-alone steam heat system.  The water temperature is broadcast to the Ultivist system for monitoring and alarm purposes.