- PURPOSE

This FSSP defines guidelines for selectively turning off lighting at Ficklen Stadium to conserve energy while maintaining safe lighting levels.

- GENERAL

Energy can be saved by selectively turning off lighting at Ficklen Stadium when there are not events.  Safe lighting levels can still be maintained.  The majority of lighting is on the north side of the stadium – the parking lot, under the stadium, the ramps to the upper deck, and the upper deck concourse.  All lighting is on timers to keep them off during the day.  Half the lights are fed from a normal power panels and half from panels that are also connected to emergency power.  The distribution of lighting throughout the areas from normal and emergency panels is relatively even.  The lighting connected to emergency power provides safe lighting levels.

- Responsibility

The Utilities Electrical Engineer has responsibility for implementation of this practice.

## PROCEDURES

- Lighting for the north side (parking lot, under the stadium, ramps to upper deck, upper deck concourse) are on timers.  The timers will be normally set to have the lights off during daylight hours.

- Breakers in panels HAE and HBE feeding power to lights will normally be left on.  These are connected to emergency power.

- Breakers in panels HA and HB feeding power to lights will normally be left off.  These are normal power.  Turn off only lighting breakers, other loads require continuous power.

- Prior to an event in the stadium that is likely to create a need for full lighting levels, the lighting breakers in panels HA and HB will be turned on.  After the event, preferably immediately after the stadium is vacated and not later than the next workday, the breakers will be turned off again.