- PURPOSE

The purpose of this plan is to optimize energy conservation while maintaining adequately conditioned space.

- HVAC OPERATING SCHEDULE

The following schedule represents the time that each air-handling unit (AHU) shall condition its corresponding space:

AHU	SCHEDULE

All	** 24hrs/day, 7 days/week **

- ENERGY OPERATING DESCRIPTION

  - EAHEC – Description

The EAHEC Modular Unit is a single story building that houses the Academic – Adolescent Psychiatry and Nursing department. The building is approximately 3,168 sq ft and is served by 2 Ruud Package Heat Pumps.

  - HVAC Supply

AHU#		Location 		Area Served

HP-1		Outside		Mobile unit

HP-2		Outside		Mobile unit

  - HVAC Control

The HVAC systems are controlled by standard thermostats and are not currently connected to the Johnson Controls Metasys System.

    - Thermostats

All AHU’s are controlled by standard thermostats, which are located in the controlled and conditioned area.

    - Set Points

Set points are adjustable at the thermostat.

    - Unoccupied Temperature Setback

These units are not equipped with any unoccupied features since they run 24hrs/day, 7 days/week.

    - Deck Control

There are no hot deck/cold deck capabilities.

  - Chilled Water Supply

N/A

  - Heating Water Supply

N/A

  - Special Operations/Instructions

There are no special operations associated with this building.