- PURPOSE

The purpose of this plans is to optimize energy conservation while maintaining adequately conditioned space.

- HVAC OPERATING SCHEDULE

The following schedule represents the time that each air-handling unit (AHU) shall condition its corresponding space:

AHU	SCHEDULE

All	** 24hrs/day, 7 days/week **

- ENERGY OPERATING DESCRIPTION

- Medical Pavilion #1

  - Medical Pavilion #1 – Description

The Medical Pavilion #1 is a single story building that operates as a clinic. This building is currently undergoing major renovation. The building is approximately 1,261 sq ft and is served by 1 Amana package unit Gas Pack.

  - HVAC Supply

AHU#		Location 		Area Served

GP-1		Mech Room		Offices

  - HVAC Control

The HVAC system is controlled by a standard thermostat and is not currently connected to the Johnson Controls Metasys System.

    - Thermostats

All AHU’s are controlled by standard thermostats, which are located in the controlled and conditioned area.

    - Set Points

Set points are adjustable at the pneumatic thermostat.

    - Unoccupied Temperature Setback

These units are not equipped with any unoccupied features since they run 24hrs/day, 7 days/week.

    - Deck Control

N/A

  - Chilled Water Supply

N/A

  - Heating Water Supply

N/A

  - Special Operations/Instructions

There are no special operations associated with this building.

- Medical Pavilion #2

  - Medical Pavilion #2 – Description

The Medical Pavilion #2 is a single story building that operates as a clinic. The building is approximately 2,171 sq ft and is served by a 2 air-handler, 1 condenser split system.

  - HVAC Supply

AHU#		Location 		Area Served

AHU-1	Mech Room		Offices

AHU-2	Mech Room		Offices

  - HVAC Control

The HVAC system is controlled by a standard thermostat and is not currently connected to the Johnson Controls Metasys System.

      - Thermostats

All AHU’s are controlled by standard thermostats, which are located in the controlled and conditioned area.

      - Set Points

Set points are adjustable at the thermostat.

      - Unoccupied Temperature Setback

These units are not equipped with any unoccupied features since they run 24hrs/day, 7 days/week.

      - Deck Control

N/A

  - Chilled Water Supply

N/A

  - Heating Water Supply

N/A

  - Special Operations/Instructions

There are no special operations associated with this building.

- Medical Pavilion #3

  - Medical Pavilion #3 – Description

The Medical Pavilion #3 is a single story building that operates as a clinic. The building is approximately 1,101 sq ft and is served by 1 split system.

  - HVAC Supply

AHU#		Location 		Area Served

AHU-1	Mech Room		Offices

  - HVAC Control

The HVAC system is controlled by a standard thermostat and is not currently connected to the Johnson Controls Metasys System.

    - Thermostats

All AHU’s are controlled by standard thermostats, which are located in the controlled and conditioned area.

    - Set Points

Set points are adjustable at the pneumatic thermostat.

    - Unoccupied Temperature Setback

These units are not equipped with any unoccupied features since they run 24hrs/day, 7 days/week.

    - Deck Control

N/A

  - Chilled Water Supply

N/A

  - Heating Water Supply

N/A

  - Special Operations/Instructions

There are no special operations associated with this building.

- Medical Pavilion #4

  - Medical Pavilion #4 – Description

The Medical Pavilion #4 is a single story building that operates as a clinic. The building is approximately 1,400 sq ft and is served by a 2 air-handler, 1 condenser split system.

  - HVAC Supply

AHU#		Location 		Area Served

AHU-1	Mech Room		Offices

AHU-2	Mech Room		Offices

  - HVAC Control

The HVAC system is controlled by a standard thermostat and is not currently connected to the Johnson Controls Metasys System.

    - Thermostats

All AHU’s are controlled by standard thermostats, which are located in the controlled and conditioned area.

    - Set Points

Set points are adjustable at the thermostat.

    - Unoccupied Temperature Setback

N/A

    - Deck Control

N/A

  - Chilled Water Supply

N/A

  - Heating Water Supply

N/A

  - Special Operations/Instructions

There are no special operations associated with this building.

- Medical Pavilion #5

  - Medical Pavilion #5 – Description

The Medical Pavilion #5 is a single story building that operates as a clinic. The building is approximately 2,222 sq ft and is served by 2 split system air handling units.

  - HVAC Supply

AHU#		Location 		Area Served

AHU-1	Mech Room		Offices

AHU-2	Mech Room		Offices

  - HVAC Control

The HVAC system is controlled by pneumatic thermostats and is not currently connected to the Johnson Controls Metasys System.

    - Thermostats

All AHU’s are controlled by pneumatic thermostats, which are located in the controlled and conditioned area.

    - Set Points

Set points are adjustable at the pneumatic thermostat.

    - Unoccupied Temperature Setback

These units are not equipped with any unoccupied features since they run 24hrs/day, 7 days/week.

    - Deck Control

N/A

  - Chilled Water Supply

N/A

  - Heating Water Supply

N/A

  - Special Operations/Instructions

There are no special operations associated with this building.

- Medical Pavilion #7

  - Medical Pavilion #7 – Description

The Medical Pavilion #7 is a single story building that operates as a clinic. The building is approximately 869 sq ft and is served by a 3-ton York split system.

  - HVAC Supply

AHU#		Location 		Area Served

AHU-1	Mech Room		Offices

  - HVAC Control

The HVAC system is controlled by pneumatic thermostats and is not currently connected to the Johnson Controls Metasys System.

    - Thermostats

All AHU’s are controlled by pneumatic thermostats, which are located in the controlled and conditioned area.

    - Set Points

Set points are adjustable at the pneumatic thermostat.

    - Unoccupied Temperature Setback

These units are not equipped with any unoccupied features since they run 24hrs/day, 7 days/week.

    - Deck Control

N/A

  - Chilled Water Supply

N/A

  - Heating Water Supply

N/A

  - Special Operations/Instructions

There are no special operations associated with this building.

- Medical Pavilion #9

  - Medical Pavilion #9 – Description

The Medical Pavilion #9 is a single story building that operates as a clinic. The building is approximately 1,218 sq ft and is served by 2 York 3-ton split systems.

  - HVAC Supply

AHU#		Location 		Area Served

AHU-1	Mech Room		Offices

AHU-2	Mech Room		Offices

  - HVAC Control

The HVAC system is controlled by pneumatic thermostats and is not currently connected to the Johnson Controls Metasys System.

    - Thermostats

All AHU’s are controlled by pneumatic thermostats, which are located in the controlled and conditioned area.

    - Set Points

Set points are adjustable at the pneumatic thermostat.

    - Unoccupied Temperature Setback

These units are not equipped with any unoccupied features since they run 24hrs/day, 7 days/week.

    - Deck Control

N/A

  - Chilled Water Supply

N/A

  - Heating Water Supply

N/A

  - Special Operations/Instructions

There are no special operations associated with this building.

- Medical Pavilion #10

  - Medical Pavilion #10 – Description

The Medical Pavilion #10 is a single story building that operates as a clinic. The building is approximately 1,326 sq ft and is served by a 4-ton York split system.

  - HVAC Supply

AHU#		Location 		Area Served

AHU-1	Mech Room		Offices

  - HVAC Control

The HVAC system is controlled by pneumatic thermostats and is not currently connected to the Johnson Controls Metasys System.

    - Thermostats

All AHU’s are controlled by pneumatic thermostats, which are located in the controlled and conditioned area.

    - Set Points

Set points are adjustable at the pneumatic thermostat.

    - Unoccupied Temperature Setback

These units are not equipped with any unoccupied features since they run 24hrs/day, 7 days/week.

    - Deck Control

N/A

  - Chilled Water Supply

N/A

  - Heating Water Supply

N/A

  - Special Operations/Instructions

There are no special operations associated with this building.