- PURPOSE

The purpose of this plan is to optimize energy conservation while maintaining adequately conditioned space.

- SYSTEM DESCRIPTION

Messick Theatre Arts Center is an two story classroom, office theatre building conditioned by two chillers and shell and tube heat exchanger using a four pipe system.

- AIR HANDLING UNITS

AHU#	RM#	Area Supplied

AHU-A1	chiller room	costume shop

AHU-A2	chiller room	McGinnis Theatre

AHU-B1	1st floor mechanical 	1st floor south offices

AHU-B2	1st floor mechanical	1st floor north offices

AHU-B3	2nd floor mechanical	2nd floor S classrooms

AHU-B4	2nd floor mechanical	2nd floor N classrooms

AHU-C5	1st floor mechanical 	1st floor E studio

AHU-C6	1st floor mechanical	1st floor E studio

AHU-C7	2nd floor mechanical	2nd floor W studio

AHU-C8	2nd floor mechanical	2nd floor E studio

AHU-C9	1st floor mechanical	1st floor W studio

AHU-D10	west mechanical	studio theatre

AHU-D11	east mechanical	studio theatre

AHU-D12	east mechanical	dressing room

AHU-E1	1st floor mechanical	1st floor prop shop

AHU-E2	1st floor mechanical	2nd floor prop shop

- HVAC CONTROLS

  - SEQUENCE OF OPERATION

The HVAC system is controlled by an Invensys DMS-3500 system, connected to the Ethernet and an Ultivist operator workstation at the Steam Plant for control and alarm monitoring.

    - AHU-A1 & A2 air-handlers are controlled by the BAS.

    - AHU-A1 & A2 utilize full economizer operation.

    - AHU-A2 supply air temperature is reset based on return air temperature.  The reset is set up to utilize energy as much as possible.

  - LOAD MANAGEMENT

There is no load management on this building.

- COOLING SYSTEM

The cooling consists of two Carrier reciprocating chillers and shares a cooling tower with the Wright building chiller.  The chillers are controlled by the BAS.

- HEATING SYSTEM

A tube and shell converter provides the hot water for heat with a circulator pump staged by outdoor air temperature.  The BAS adjusts the temperature reset based on outdoor air temperature.

- SPECIAL OPERATING INSTRUCTIONS