- PURPOSE

The purpose of this plan is to optimize energy conservation while maintaining adequately conditioned space.

- SYSTEM DESCRIPTION

Willis building is an administrative office building with one air conditioning unit with hot water coils.

- AIR HANDLING UNITS

AHU#	RM#	Area Supplied

AHU-1	1st Floor Mech. Rm.	1st floor

- HVAC CONTROLS

  - SEQUENCE OF OPERATION

The HVAC system is controlled by an Invensys DMS-3500 system, connected to the Ethernet and an Ultivist operator workstation at the Steam Plant for control and alarm monitoring.

    - AHU-1 is a multizone with DX cooling and hot water heat. The air-handler is controlled by the BAS.

    - The lobby zone is controlled by a zone sensor and controlled by the BAS.

    - Pneumatic thermostats control the north and south zones and each office has its own thermostat and reheat coil to maintain space temperature.

    - The two enter zones (auditorium and back office area) are controlled by pneumatic thermostats and do not utilize reheat.

  - LOAD MANAGEMENT

There is no load management on this building.

- COOLING SYSTEM

The cooling consists of a Carrier split system DX unit.

- HEATING SYSTEM

The heating system is a gas-fired boiler utilizing a stand-alone reset system.

- SPECIAL OPERATING INSTRUCTIONS