- GENERAL

# The maintenance of utility systems shall be the responsibility of Facilities Services.  Facilities Services has fiscal responsibility for the main utility systems.

- PURPOSE

# The purpose of this FSSP is to define the borders of the main utility systems.

- Responsibilities

  - Facilities Services fiscal responsibility for the system will end at the following points (unless specific written exceptions are agreed upon) for non-E&G buildings:

    - Electrical Power – at the high voltage connection to the building transformer.

    - Water – at the inlet of the building meter.  At the building line if metered inside the building.  Facilities Services is not responsible for the hot water lines between Slay and Umstead and between Cotton and Fleming.

    - Fire sprinkler water – at the meter.  If no meter, at the inlet side of the backflow preventer.

    - Sanitary Sewer – at the manhole where the lateral to the building terminates.

    - Steam/Condensate - at (and including) the isolation valve in a manhole or tunnel.  At the building line if there is not an isolation valve at the main line.  For condensate, where it ties back into the campus distribution system.

    - Chilled Water – at (and including) the building isolation valves.  At the building line if there is not an isolation valve at the main line.  For chilled water return, where it ties back into the campus distribution system.

    - Fire Alarm – Facilities Services is responsible for only the Silent Knight receiver.

    - Storm water – at the building line.

    - Irrigation Water – at the inlet to the farthest upstream irrigation water meter or backflow preventer device.

    - Natural Gas – to the downside of the meter.

    - Telephone and data – Facilities Services has no responsibility for this system.

    - Cable TV – Facilities Services has no responsibility for this system.

  - The building line includes any permanent structure to the building (e.g. porches, patios, breezeways, etc.)

  - Other than gas meters, all other meters are maintained by Facilities Services but fiscal responsibility is by the user.

  - Facilities Services will maintain master drawings showing the sanitary sewer, steam/condensate, and chilled water system boundaries.

  - Exceptions must be approved by the Senior Associate Vice Chancellor for Campus Operations.