- GENERAL

Lighting is a significant user of electricity and is a significant portion of the University’s electrical bill.  Upgrading to higher efficiency lighting reduces usage and therefore electrical costs but the replacement cost offsets the savings.  Maintenance replacement is a cost effective way of upgrading.

- PURPOSE

This FSSP provides guidelines for the maintenance upgrading of interior lighting.  It applies to general area lighting not necessarily to specialty lighting such as dimmable lighting.

- PROCEDURES

  - When incandescent bulbs burn out, they should be replaced with compact fluorescent lamps (CFL).  Where a CFL does not fit, consideration should be given to replacing the fixture with a fluorescent.

  - When an incandescent fixture must be replaced, replace it with a fluorescent fixture where practical (e.g. a room with one fixture, a room with two fixtures replace both).

  - When magnetic ballast fails, replace it with electronic ballast and T8 lamps.  Where it is more cost effective, the fixture should be replaced.

  - When electronic T12 ballast fails, replace it with electronic ballast and T8 lamps. Where it is more cost effective, the fixture should be replaced.