Eye and Face Protection - appropriate eye and/or face protection is required when employees are in areas where there is exposure to eye and face hazards from flying particles, molten metal, liquid chemicals, acids, caustic liquids, chemical gases or vapors or potentially injurious light radiation.  All eye protection must be ANSI approved.

| ACTIVITY | HAZARD | TYPE OF PPE | AFFECTED DEPARTMENTS/JOB TITLES |
| --- | --- | --- | --- |
| IMPACT chipping, grinding, masonry work, woodworking, sawing, drilling, chiseling, scraping, sanding, weed eating, mowing, visiting construction sites, etc. | Flying fragments, objects, large chips, particles, sand, dirt, etc. | Spectacles with side protection, goggles, or face shield. Face shields should be used for severe exposure and can only be worn over primary eye protection (glasses or goggles). Persons whose vision requires the use of prescription lenses must wear either protective devices fitted with prescription lenses or protective devices designed to be worn over regular prescription eye wear. | Facilities Planning, Design & Construction - Facility Const. Eng. II, Facility Mech. Eng. I, Facility Architect II and Cnst. Ren. Dsgn. Tech II. Carpentry Shop - Carpenter Sup. II, Roofer, Maint. Mech. I, Locksmith II, Locksmith III, Trades Worker III and Carpenter II. Paint Shop - Painter Supervisor and Painter. Garage - Mechanic Sup. I, Mechanic I and Mechanic II. Masonry Shop - Mason Sup., Mason I, Mason II, Maint. Mech. I and Trades Worker III. Grounds - Grounds Sup. I, Grounds Worker, Gen. Util. Worker and Laborer. Steam Plant - Steam Plant Sup. II, Steam Plant Supervisor I, Maint. Mech. IV and Boiler Operator II. Plumbing Shop - Plumber Sup., Maint. Mech. IV and Plumber II. HVAC Shop - HVAC Sup. II, HVAC Sup. I, Maint. Mech. II, HVAC Technician, HVAC Mech. and Plumber II. Electrical Shop - Electrical Sup. II, Elec. Sup. I, Electrician II and Maint. Mech. II |
| CHEMICALS Chemical handling/testing, cleaning sanitary sewers, painting, checking batteries, pesticide application, etc. | Splash, irritating mists, etc. | Goggles. For severe exposure use face shield. Face shields can only be worn over primary eye protection (glasses or goggles). | Housekeeping Services - Hskg. Sup. I, II, and III, Hskg. Team Leader, Oper. Mgr. Hskg. Svs., and Housekeepers. Grounds - Grounds Sup. I, Grounds Worker, Gen. Util. Worker and Laborer. Garage - Mechanic Sup. I, Mechanic I and Mechanic II. Masonry Shop - Mason Sup., Mason I, Mason II, Maint. Mech. I and Trades Worker III. Paint Shop - Painter Supervisor and Painter. Plumbing Shop - Plumber Sup., Maint. Mech. IV and Plumber II. HVAC Shop - HVAC Sup. II, HVAC Sup. I, Maint. Mech. II, HVAC Technician, HVAC Mech. and Plumber II. Steam Plant - Steam Plant Sup. II, Steam Plant Supervisor I, Maint. Mech. IV and Boiler Operator II. |
| DUST Woodworking, buffing, particularly dusty conditions, etc. | Nuisance dust | Goggles | Housekeeping Services - Hskg. Sup. I, II, and III, Hskg. Team Leader, Oper. Mgr. Hskg. Svs., and Housekeepers. Carpentry Shop - Carpenter Sup. II, Roofer, Maint. Mech. I, Locksmith II, Locksmith III, Trades Worker III and Carpenter II. Grounds - Grounds Sup. I, Grounds Worker, Gen. Util. Worker and Laborer. |
| LIGHT/RADIATION Electric arc welding, gas welding, cutting, torch soldering, etc. | Optical radiation | Welding helmets, welding shields or welding goggles with appropriate shades. | Plumbing Shop - Plumber Sup., Maint. Mech. IV and Plumber II. HVAC Shop - HVAC Sup. II, HVAC Sup. I, Maint. Mech. II, HVAC Technician, HVAC Mech. and Plumber II. Steam Plant - Steam Plant Sup. II, Steam Plant Supervisor I, Maint. Mech. IV and Boiler Operator II. Garage - Mechanic Sup. I, Mechanic I and Mechanic II. |

Respiratory Protection - appropriate respiratory protection is required when employees are in areas where effective engineering controls are not feasible to protect the health of the employee from harmful dusts, fogs, fumes, mists, gases, smokes, sprays, or vapors.  All required respirators must be NIOSH/MSHA approved.

| ACTIVITY | HAZARD | TYPE OF PPE | AFFECTED DEPARTMENTS/JOB TITLES |
| --- | --- | --- | --- |
| (Required) Asbestos O&M Activities, Welding/Cutting in Confined Spaces, Spray Painting, Pesticide Application, Entry into Brody Hood Exhaust Area, etc. | Asbestos, welding fumes, organic vapors, paint spray, pesticides, assorted chemicals, radioisotopes and biological contaminants | Negative pressure half and full face air-purifying respirators with HEPA, Organic Vapor or other appropriate filter/cartridge; Positive pressure powered full face and hood/helmet air purifying respirators with HEPA or other appropriate filter/cartridge; or Self-Contained Breathing Apparatus (SCBA). | Grounds - Grounds Sup. I, Grounds Worker, Gen. Util. Worker and Laborer. Paint Shop - Painter Supervisor and Painter. Plumbing Shop - Plumber Sup., Maint. Mech. IV and Plumber II. HVAC Shop - HVAC Sup. II, HVAC Sup. I, Maint. Mech. II, HVAC Technician, HVAC Mech. and Plumber II. Steam Plant - Steam Plant Sup. II, Steam Plant Supervisor I, Maint. Mech. IV and Boiler Operator II. Masonry Shop - Mason Sup., Mason I, Mason II, Maint. Mech. I and Trades Worker III. Electrical Shop - Electrical Sup. II, Elec. Sup. I, Electrician II and Maint. Mech. II |
| (Optional but Recommended) Weed Eating, Grass Mowing, Dusting Woodworking, Masonry Work, etc. | Nuisance Dust, Pollen | Nuisance Dust Mask | Housekeeping Services - Hskg. Sup. I, II, and III, Hskg. Team Leader, Oper. Mgr. Hskg. Svs., and Housekeepers. Carpentry Shop - Carpenter Sup. II, Roofer, Maint. Mech. I, Locksmith II, Locksmith III, Trades Worker III and Carpenter II. Grounds - Grounds Sup. I, Grounds Worker, Gen. Util. Worker and Laborer. Masonry Shop - Mason Sup., Mason I, Mason II, Maint. Mech. I and Trades Worker III. |

Head Protection - appropriate head protection is required when employees are in areas where there is a potential for injury to the head from falling or moving objects or when they are exposed to electrical conductors which could be contacted by the head.  All head protection must be ANSI approved.

| ACTIVITY | HAZARD | TYPE OF PPE | AFFECTED DEPARTMENTS/JOB TITLES |
| --- | --- | --- | --- |
| Tree cutting or pruning, visiting construction areas, steam tunnel entry, routine activities where an overhead hazard exists or there is a possibility of falling objects, etc. | limbs and branches, construction hazards, bump hazards, falling objects | ANSI approved hard hats, hard caps or bump caps | Facilities Planning, Design & Construction - Facility Const. Eng. II, Facility Mech. Eng. I, Facility Architect II and Cnst. Ren. Dsgn. Tech II. Carpentry Shop - Carpenter Sup. II, Roofer, Maint. Mech. I, Locksmith II, Locksmith III, Trades Worker III and Carpenter II. Paint Shop - Painter Supervisor and Painter. Masonry Shop - Mason Sup., Mason I, Mason II, Maint. Mech. I and Trades Worker III. Grounds - Grounds Sup. I, Grounds Worker, Gen. Util. Worker and Laborer. Steam Plant - Steam Plant Sup. II, Steam Plant Supervisor I, Maint. Mech. IV and Boiler Operator II. Plumbing Shop - Plumber Sup., Maint. Mech. IV and Plumber II. HVAC Shop - HVAC Sup. II, HVAC Sup. I, Maint. Mech. II, HVAC Technician, HVAC Mech. and Plumber II. Electrical Shop - Electrical Sup. II, Elec. Sup. I, Electrician II and Maint. Mech. II |

Foot Protection - appropriate foot protection is required when employees are in areas where there is danger of foot injuries due to falling and rolling objects, slip hazards or objects piercing the sole, and where employees are exposed to electrical hazards.  All foot protection must be ANSI approved.

| ACTIVITY | HAZARD | TYPE OF PPE | AFFECTED DEPARTMENTS/JOB TITLES |
| --- | --- | --- | --- |
| Visiting construction areas, Lifting and transporting parts, equipment, etc., cleaning sanitary sewers and work in other wet areas, etc. | Falling and/or rolling objects, sharp objects, slip hazards | ANSI approved slip resistant steel toed shoes; waterproof boots. | Facilities Planning, Design & Construction - Facility Const. Eng. II, Facility Mech. Eng. I, Facility Architect II and Cnst. Ren. Dsgn. Tech II. Carpentry Shop - Carpenter Sup. II, Roofer, Maint. Mech. I, Locksmith II, Locksmith III, Trades Worker III and Carpenter II. Paint Shop - Painter Supervisor and Painter. Garage - Mechanic Sup. I, Mechanic I and Mechanic II. Masonry Shop - Mason Sup., Mason I, Mason II, Maint. Mech. I and Trades Worker III. Grounds - Grounds Sup. I, Grounds Worker, Gen. Util. Worker and Laborer. Steam Plant - Steam Plant Sup. II, Steam Plant Supervisor I, Maint. Mech. IV and Boiler Operator II. Plumbing Shop - Plumber Sup., Maint. Mech. IV and Plumber II. HVAC Shop - HVAC Sup. II, HVAC Sup. I, Maint. Mech. II, HVAC Technician, HVAC Mech. and Plumber II. Electrical Shop - Electrical Sup. II, Elec. Sup. I, Electrician II and Maint. Mech. II Housekeeping Services - Hskg. Sup. I, II, and III, Hskg. Team Leader, Oper. Mgr. Hskg. Svs., and Housekeepers. |

Electrical Protective Devices - appropriate electrical protective devices in the form of insulating blankets, matting, covers, line hose, gloves, and sleeves made of rubber are required when employees are in areas where there may be exposure to substantial electrical voltage.

| ACTIVITY | HAZARD | TYPE OF PPE | AFFECTED DEPARTMENTS/JOB TITLES |
| --- | --- | --- | --- |
| High voltage work on switches, transformers, switch gear, electrical manholes and other equipment | Electrical shock | Nonconductive safety shoes, rubber insulating line hose, insulating covers, insulating blankets, insulating gloves and lockout/tagout devices | Electrical Shop - Electrical Sup. II, Elec. Sup. I, Electrician II and Maint. Mech. II |

Hand Protection - appropriate hand protection is required when employees are in areas where their hands are exposed to skin absorption of harmful substances, severe cuts or lacerations, severe abrasions, punctures, chemical burns, thermal burns or harmful temperature extremes.  Appropriate gloves are dependent upon the type of chemical contaminant or physical hazard.  Special care must be taken when selecting gloves for chemical exposure to assure glove is resistant to the chemical in question.  Reference the enclosed ILC Dover Chemical Compatibility Chart.

| ACTIVITY | HAZARD | TYPE OF PPE | AFFECTED DEPARTMENTS/JOB TITLES |
| --- | --- | --- | --- |
| Handling chemicals, welding, cutting, metal working, material handling, brick laying, etc. | chemicals, sharp edges, abrasive surfaces, heat and steam | chemical resistant gloves including but not limited to vinyl, latex, rubber, nitrile, neoprene (special care must be taken when selecting gloves for chemical usage to assure they are resistant and won’t allow breakthrough to the skin), leather or other cut resistant work gloves, heat resistant gloves | Carpentry Shop - Carpenter Sup. II, Roofer, Maint. Mech. I, Locksmith II, Locksmith III, Trades Worker III and Carpenter II. Paint Shop - Painter Supervisor and Painter. Garage - Mechanic Sup. I, Mechanic I and Mechanic II. Masonry Shop - Mason Sup., Mason I, Mason II, Maint. Mech. I and Trades Worker III. Grounds - Grounds Sup. I, Grounds Worker, Gen. Util. Worker and Laborer. Steam Plant - Steam Plant Sup. II, Steam Plant Supervisor I, Maint. Mech. IV and Boiler Operator II. Plumbing Shop - Plumber Sup., Maint. Mech. IV and Plumber II. HVAC Shop - HVAC Sup. II, HVAC Sup. I, Maint. Mech. II, HVAC Technician, HVAC Mech. and Plumber II. Electrical Shop - Electrical Sup. II, Elec. Sup. I, Electrician II and Maint. Mech. II Housekeeping Services - Hskg. Sup. I, II, and III, Hskg. Team Leader, Oper. Mgr. Hskg. Svs., and Housekeepers. |

Hearing Protection - appropriate hearing protection is required when employees are in areas where there is exposure to excessive noise levels.  Protection is not required unless the employee’s time weighted average exposure exceeds 85 decibels (db) for an 8 hour exposure.  However it is recommended that appropriate hearing attenuators are provided to employees for use in all high noise areas (mechanical rooms, boiler rooms, etc.) as a precautionary measure.

| ACTIVITY | HAZARD | TYPE OF PPE | AFFECTED DEPARTMENTS/JOB TITLES |
| --- | --- | --- | --- |
| Routine maintenance activities in high noise areas, mowing grass, weed eating, blowers, other high noise equipment operation | Noise | ANSI approved ear plugs or ear muffs with appropriate noise reduction rating (NRR) | Facilities Planning, Design & Construction - Facility Const. Eng. II, Facility Mech. Eng. I, Facility Architect II and Cnst. Ren. Dsgn. Tech II. Carpentry Shop - Carpenter Sup. II, Roofer, Maint. Mech. I, Locksmith II, Locksmith III, Trades Worker III and Carpenter II. Paint Shop - Painter Supervisor and Painter. Garage - Mechanic Sup. I, Mechanic I and Mechanic II. Masonry Shop - Mason Sup., Mason I, Mason II, Maint. Mech. I and Trades Worker III. Grounds - Grounds Sup. I, Grounds Worker, Gen. Util. Worker and Laborer. Steam Plant - Steam Plant Sup. II, Steam Plant Supervisor I, Maint. Mech. IV and Boiler Operator II. Plumbing Shop - Plumber Sup., Maint. Mech. IV and Plumber II. HVAC Shop - HVAC Sup. II, HVAC Sup. I, Maint. Mech. II, HVAC Technician, HVAC Mech. and Plumber II. Electrical Shop - Electrical Sup. II, Elec. Sup. I, Electrician II and Maint. Mech. II Housekeeping Services - Hskg. Sup. I, II, and III, Hskg. Team Leader, Oper. Mgr. Hskg. Svs., and Housekeepers. |

Fall Protection - appropriate fall protection is required when employees are at risk of falling from an elevated position, as a general rule, anytime a working height of six feet or more is reached.  Appropriate fall protection must also be utilized at any height when employees are in aerial lifts, powered platforms and similar devices.

| ACTIVITY | HAZARD | TYPE OF PPE | AFFECTED DEPARTMENTS/JOB TITLES |
| --- | --- | --- | --- |
| Work exposing employee to risk of falling at heights 6 feet or greater when area is not guarded or protected by other approved form of engineering control Work at any height in aerial lifts, powered platforms, and similar devices | Fall | Personal fall arrest system consisting of anchorage, connectors, and a full-body harness with shock-absorbing lanyard or retractable lifeline “Pers | Facilities Planning, Design & Construction - Facility Const. Eng. II, Facility Mech. Eng. I, Facility Architect II and Cnst. Ren. Dsgn. Tech II. Carpentry Shop - Carpenter Sup. II, Roofer, Maint. Mech. I, Locksmith II, Locksmith III, Trades Worker III and Carpenter II. Paint Shop - Painter Supervisor and Painter. Garage - Mechanic Sup. I, Mechanic I and Mechanic II. Masonry Shop - Mason Sup., Mason I, Mason II, Maint. Mech. I and Trades Worker III. Grounds - Grounds Sup. I, Grounds Worker, Gen. Util. Worker and Laborer. Steam Plant - Steam Plant Sup. II, Steam Plant Supervisor I, Maint. Mech. IV and Boiler Operator II. Plumbing Shop - Plumber Sup., Maint. Mech. IV and Plumber II. HVAC Shop - HVAC Sup. II, HVAC Sup. I, Maint. Mech. II, HVAC Technician, HVAC Mech. and Plumber II. Electrical Shop - Electrical Sup. II, Elec. Sup. I, Electrician II and Maint. Mech. II Housekeeping Services - Hskg. Sup. I, II, and III, Hskg. Team Leader, Oper. Mgr. Hskg. Svs., and Housekeepers. |